## Slide 1: Lab03_MAZE
MAZE

## Slide 2: OUTLINE
SPEC
Algorithm
System Architecture
RTL design

## Slide 3: SPEC
Input Signal | Bit Width | Description
clk | 1 | Clock.
rst_n | 1 | Asynchronous active-low reset.
in_valid | 1 | High when input is valid.
in | 1 | High stands for path, and Low stands for wall
Output Signal | Bit Width | Description
out_valid | 1 | High when out is valid.
out | 2 | Right: 2’d0; Down: 2’d 1; Left: 2’d 2; Up: 2’d 3
The input signal in is delivered in raster scan order for 289 cycles continuously

## Slide 4
MAZE SPEC
In general, the walls can not exist in the white block
Maze examples

## Slide 5: Algorithm
核心:填死路
1.先將迷宮外圍，填一圈牆，以便於判斷死路。
2.利用三面為牆來判斷是否為死路。
3.將死路填滿後，剩下的就是唯一正確道路。

## Slide 6: System Architecture
FSM(moore machine)
IDLE
INPUT
in_valid
!in_valid
in_valid
WALL
cnt_wall<45
!in_valid
RIGHT
DOWN
LEFT
UP
in[0][col+1]
!in[0][col+1]
hit wall
hit wall
hit wall
hit wall
out = 0
out = 1
out = 2
out = 3

## Slide 7: RTL design
FSM

## Slide 8
判斷死路:三面為牆
A=in[row][col+1], B=in[row+1][col], C=in[row][col-1], D= in[row-1][col].
死路=A+
++
A | B | C | D | 死路
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 9
output
out_valid
out

## Slide 10: THANK